## Slide 1: Digital IC Design
Department of Electronics Engineering, Chang Gung University
Hyperbolic Rotation:
Vectoring Mode
Presented by: 蕭銘宏 B1027236

## Slide 2: Outline
Department of Electronics Engineering, CGU
Algorithm
Floating/Fixed Point Simulation
RTL Implementation
Synthesis Result

## Slide 3: Algorithm
Digital IC Design Department of Electronics Engineering, CGU
An example for computing arctanh using vectoring mode in hyperbolic rotation.
Let
Derived through multiple iterations.
Notes: Cordic 有分三種座標、兩種模式，我做的是 Hyperbolic 座標下的 Vectoring mode，以反雙曲正切函數(arctanh)的計算為期末專題。
---
tanh: hyperbolic tangent

## Slide 4: Algorithm
Digital IC Design Department of Electronics Engineering, CGU
An example for computing arctanh using vectoring mode in hyperbolic rotation.
Let
Derived through multiple iterations.
Notes: Cordic 有分三種座標、兩種模式，我做的是 Hyperbolic 座標下的 Vectoring mode，以反雙曲正切函數(arctanh)的計算為期末專題。
---
tanh: hyperbolic tangent

## Slide 5
Digital IC Design Department of Electronics Engineering, CGU
An example for computing arctanh using vectoring mode in hyperbolic rotation.
Let
Derived through multiple iterations.
Floating/Fixed Point Simulation
Notes: Cordic 有分三種座標、兩種模式，我做的是 Hyperbolic 座標下的 Vectoring mode，以反雙曲正切函數(arctanh)的計算為期末專題。
---
tanh: hyperbolic tangent

## Slide 6: Introduction
Computer-Aided VLSI System Design Graduate Institute of Electronics Engineering, NTU
請完成一Gauss-Seidel Iteration Machine(GSIM)的電路設計來求出多元線性聯立方程式(Linear Equation)之解
如下圖所示，矩陣A、B為已知之整數值，待求矩陣X之解
– 在此專題中，N 固定為16

## Slide 7: Introduction
Computer-Aided VLSI System Design Graduate Institute of Electronics Engineering, NTU
請完成一Gauss-Seidel Iteration Machine(GSIM)的電路設計來求出多元線性聯立方程式(Linear Equation)之解
如下圖所示，矩陣A、B為已知之整數值，待求矩陣X之解
– 在此專題中，N 固定為16

## Slide 8
Computer-Aided VLSI System Design
Graduate Institute of Electronics Engineering, NTU
Matrix Memory
Solution Memory
GSIM.v
i_clk
i_reset
o_proc_done
i_matrix_num 5
i_module_en
i_mem_dout_vld
i_mem_rrdy
i_mem_dout 256
o_x_wen
o_x_addr
9
o_x_data
32
Block Diagram
testbed.v
o_mem_rreq
o_mem_addr 10

## Slide 9: Computer-Aided VLSI System Design
Graduate Institute of Electronics Engineering, NTU
Input/Output
 | Signal Name | I/O | Width | Simple Description | 
 | i_clk | I | 1 | 本系統為同步於時脈正緣之同步設計。 (註: Host端採clk正緣時送資料。) | 
 | i_reset | I | 1 | 高位準”非”同步(active high asynchronous)之系統重置信號。 | 
 | i_module_en | I | 1 | 模組控制訊號。當為high時模組操作有效。 | 
 | i_matrix_num | I | 5 | 要計算矩陣數量。 | 
 | o_proc_done | O | 1 | 運算完成訊號。當將所有要求的解輸出後，須將此訊號設為high代表運算完成，並在i_module_en為0時再設為low。 | 
 | o_mem_rreq | O | 1 | 要讀取matrix memory時須設為high。 | 
 | o_mem_addr | O | 10 | 要讀取matrix memory之位址。 | 
 | i_mem_rrdy | I | 1 | 要讀取matrix memory之ready訊號。為high時代表此時可讀取 memory data。 | 
 | i_mem_dout | I | 256 | Matrix memory data 。 共 有 16 筆 16-bit 資料 ， 採 用 2’s complement表示。細節請參考。 | 
 | i_mem_dout_vld | I | 1 | Matrix memory data有效訊號。為high時代表此時i_mem_dout 有效。 | 
 | o_x_wen | O | 1 | 輸出資料有效之控制訊號。當為High時，表示目前輸出的資料為有效的。 | 
 | o_x_addr | O | 9 | 輸出矩陣解之位址。 | 
 | o_x_data | O | 32 | 要輸出之矩陣解。採用2’s complement表示(16-bit整數+16-bit 小數)。 | 

## Slide 10: Gauss-Seidel Iteration Machine
Computer-Aided VLSI System Design Graduate Institute of Electronics Engineering, NTU
所求多元線性聯立方程式如下式所示
欲求x1, x2, …, xN的值，可以將上式整理成底下式子
(1)
(2)

## Slide 11: Gauss-Seidel Iteration Machine
Computer-Aided VLSI System Design Graduate Institute of Electronics Engineering, NTU
Gauss-Seidel Iteration就是將(2)式作相同的動作數次的疊代，其行為如下式所示，反覆地疊代數次後，即可將所有待求的x值收斂在某一個值，該x值即為所求，
– 在此專題中，疊代次數固定為16。
(3)

## Slide 12
Computer-Aided VLSI System Design
Graduate Institute of Electronics Engineering, NTU
Data Presentation
2’s complement
– Ex. 16-bit(2-bit整數+14-bit小數) -> S1.14
矩陣A及b都是放在外面的memory中，由設計者決定怎麼讀取
a1,1 a2,1
a16,1
a1,2 a2,2
a16,2
a16,16
a1,16 a2,16
A =
b =
a16,1
1/a1,1
a2,1
a16,2
a1,2
1/a2,2
1/a16,16
a1,16
a2,16
b16
b1
b2
b1 b2
b16
...
...
...
...
...
...
...
0
1
15
16
addr
...
Matrix Memory (1024x256 bits)
S15
S1.14
S15
Data presentation:
...
...
...
...
...

## Slide 13: Order for Computation
Computer-Aided VLSI System Design Graduate Institute of Electronics Engineering, NTU
Integer asymmetric saturation
  若發生overflow，則取其能表示的最大值/最小值來做為結果
Fractional truncation
  小數部分當bit-width變小時直接truncate即可(不用四捨五入)

## Slide 14
Computer-Aided VLSI System Design
Graduate Institute of Electronics Engineering, NTU
Initialization
X 初始化方式如下
S15.16
bN: S15 1/aNN: S1.14
S17.14
Integer asymmetric saturation

## Slide 15: Matrix Storage
Computer-Aided VLSI System Design Graduate Institute of Electronics Engineering, NTU
假設要處理3個矩陣，則其儲存在memory的順序如下
A1 -> b1 -> A2 -> b2 -> A3 -> b3
A1
addr
0
16
17
Matrix Memory (1024x256 bits)
b1
A2
b2
A3
b3
33
34
40

## Slide 16: Result Output
Computer-Aided VLSI System Design Graduate Institute of Electronics Engineering, NTU
將矩陣解輸出儲存至solution memory
– 一次只輸出32-bit答案
X =
x1 x2
x16
...
x
1
x2
x16
Solution Memory
addr (512x32 bits)
...
0
1
15
X2
X3
Solution Memory
addr (512x32 bits)
0
X1
16
32
如果要解的矩陣有三個
(a)
(b)

## Slide 17: Specification
Computer-Aided VLSI System Design Graduate Institute of Electronics Engineering, NTU
Only worst-case library is used for synthesis.
The synthesis result of data type should NOT include any Latch.
The slack for setup-time should be non-negative.
No any timing violation and glitches for the gate level
simulation and post-layout simulation.

## Slide 18
Computer-Aided VLSI System Design
Graduate Institute of Electronics Engineering, NTU
Waveform
(2)o_mem_addr
i_mem_rrdy
(3)
(4)
0
i_clk
i_reset
i_module_en
(1)
i_matrix_num 0
o_proc_done
o_mem_rreq
i_mem_dout
i_mem_dout_vld
o_x_wen
o_x_addr
o_x_data
3
a0
a1
a2 a3
a4
0
d0
0
d1 d2 d3
0
0
0
3
0
a255
0
0
0
d1 d2 d3
d1 d2 d3
0
0

## Slide 19
Computer-Aided VLSI System Design
Graduate Institute of Electronics Engineering, NTU
Handshake
0
i_clk
o_mem_rreq
o_mem_addr
i_mem_rrdy
i_mem_dout
i_mem_dout_vld
a0
a1
a2 a3
a4
0
d0
0
d1 d2 d3
0
o_mem_rreq & i_mem_rrdy -> addr received
Guarantee next cycle, data valid
i_mem_rrdy在每個cycle為1的機率為0.5

## Slide 20: Computer-Aided VLSI System Design
Graduate Institute of Electronics Engineering, NTU
Design Flow
NCVerilog sim

## Slide 21: Specifications for APR (1)
Computer-Aided VLSI System Design Graduate Institute of Electronics Engineering, NTU
只需做Marco layout 即不用包含IO Pad 、 Bonding Pad)
set_aspect_ratio 0.6
VDD 與 VSS Power Ring 寬度請各設定為 2um 只須做一組
不需加Dummy Metal
Power Stripe 務必至少加一組，其VDD 、 VSS 寬度各設定為 2um
– Power Stripe 垂直方向至少一組，水平方向可不加

## Slide 22: Specifications for APR (2)
Computer-Aided VLSI System Design Graduate Institute of Electronics Engineering, NTU
務必要加Power Rail (follow pin)
Core Filler 務必要加
APR 後之GDSII 檔案務必產生
完成APR DRC/LVS 完全無誤
記得先產生GSIM.ioc，再重新讀取該檔來設定 pin position

## Slide 23: Grading Policy (1)
Computer-Aided VLSI System Design Graduate Institute of Electronics Engineering, NTU
Baseline 50% + Performance 35% + Report 15%
Item |  | % | Description
RTL Simulation |  | 10 | 通過提供的5個pattern
Verification |  | 10 | Coverage (line 100%), nLint no Error
Synthesis |  | 15 | EPS, Pass gate-level sim
APR |  | 15 | Finish APR with no DRC/LVS errors Pass post-layout simulation
Performance | Area, time | 20 | Area x Time
 | Power | 15 | 10:Compare active window, total energy 5: idle, idle_after_active
Report |  | 15 | 

## Slide 24: Grading Policy (2)
Computer-Aided VLSI System Design Graduate Institute of Electronics Engineering, NTU
Baseline 50% + Performance 35% + Report 15%
Violation | Penalty
不符合 design specification | Performance*0.5
無法通過hidden pattern | Performance*0.5
沒有考慮random i_mem_rrdy | Performance不評分
違反繳交格式與規則 | 總分-3

## Slide 25: Grading Policy (3)
Computer-Aided VLSI System Design Graduate Institute of Electronics Engineering, NTU
RTL Simulation 注意事項
  沒有考慮random i_mem_rrdy但能通過tb0~tb4也可以拿到所有分數
Coverage 注意事項
  Coverage只針對執行tb3的line coverage的結果來進行評分()
Synthesis 注意事項
  沒有做EPS但能過gate-level simulation還是能拿到所有分數
  有做EPS除了能比較有機會做出比較小的面積以外，Report分數也會
看有沒有使用EPS進行評分
Power注意事項
  只需跑gate-level tb4即可
  評分會用Energy來進行評分

## Slide 26: Performance (1)
Computer-Aided VLSI System Design Graduate Institute of Electronics Engineering, NTU
Score = Area × Time
– Area
– Time
innovus #> analyzeFloorplan

## Slide 27
Computer-Aided VLSI System Design
Graduate Institute of Electronics Engineering, NTU
Performance (2)
Power
  idle_power和 idle_after_active_power請根據模擬情形進行調整(參考 MTK講義p12)
  若idle_power和 idle_after_active_power的 difference超過5%，此部分扣3分

## Slide 28
Computer-Aided VLSI System Design
Graduate Institute of Electronics Engineering, NTU
Report
需要包含底下幾個項目
  架構設計
  硬體優化方法 (latency, area, power…)
  nLint report with 0 errors
  Coverage result
  Congestion map (如果有跑EPS流程)
  Primetime power report (Gate-level)
  Layout
  Area result
  Performance 表格

## Slide 29
Computer-Aided VLSI System Design
Graduate Institute of Electronics Engineering, NTU
Submission (1)
GSIM.v
GSIM_syn.v
GSIM_syn.sdf
GSIM_pr.v
GSIM_pr.sdf
GSIM.gds
GSIM_final.tar (archive of the design database directory)
report.pdf
all other design files included in your design for rtl simulation (optional)

## Slide 30: Submission (2)
Computer-Aided VLSI System Design Graduate Institute of Electronics Engineering, NTU
Due Friday, Jan. 14, 23:59
Final project presentation (MTK experience sharing)
– Date: January 18, 2021